Lista de componentes.
Circuitos integrados
Nucleo procesador
Numero parte / (Part number)	Función	Encapsulado	Fabricante	Costo
EC28J60-I/SO	Controlador ethernet 10Base-T	SOIC-28	Microchip	2.83 $ por unidad
SN75ALS162DWR	Transceiver bus GPIB	SOIC-24	Texas Instruments	3,29 $ por 1k unidades
SN75ALS160DWR	Transceiver bus GPIB	SOIC-24	Texas Instruments	1,12 $ por 1k unidades
TM4C129ENCPDT	Microcontrolador ARM Cortex M4F, 32 bit, 120 MHz	TQFP-128	Texas Intruments	8.66 $ por 1k unidades
TM4C123GH6PZI7	ARM Cortex-M4F 32-bit based MCU
PIC18F45K50T-I/PT	Microcontrolador PIC18, 8bits, USB	TQFP-44	Microchip	2,76 $ por unidad
LPC1768			NXP
MK80FN256	Kinetis K80: 150MHz Cortex-M4F	LQFP-100	NXP
MKL43Z256	Kinetis KL43: 48MHz Cortex-M0+		NXP

Microcontrolador Central
Versión 1: núcleo de 32 bits
MCU	Descripción	Flash (kB)	SRam (kB)	Package	USB	Ethernet	Frec / (MHz)
TM4C129ENCPDT	IoT enabled High performance 32-bit ARM® Cortex®-M4F based MCU	1024	256	TQFP-128	D,H/D,OTG	MAC+PHY	120 MHz
LPC1768FBD1	ARM Cortex-M3	512	64	LQFP100	D/H/OTG	MAC	100MHz
MKL26Z256VLL4	Kinetis KL26 Cortex-M0+	256	32	LQFP-100	FS	No	48 MHz

Microcontrolador Central
Versión 1: núcleo de 8 bits
MCU	Descripción	Flash (kB)	SRam (kB)	Package	USB	Ethernet	Frec / (MHz)
PIC18F4550	PIC MCU 8 bits	32	2	DIP40	Si	No	48

Controlador Ethernet
Externo
Controlador	Fabricante	Ethernet	Encapsulado	On chip eth buffer	Interfaz	Costo unitario ($)
ENC28J60	Microchip	10 Base-T	SPDIP-28 / SOIC-28	8 kB	SPI	3,03 / 2,88 (Microchip)
ENC424J600	Microchip	10/100 Base-T	TQFP-44	24 kB	SPI	3,58 (Microchip)
ENC624J600	Microchip	10/100 Base-T	TQFP-64	24 kB	SPI	3,87 (Microchip)
PIC18F67J60	Microchip	10/100/1000 Base-T	TQFP-64	8 kB		4,55 (Microchip)
W5500	WIZnet	10/100	TQFP-48	32 kB	SPI
CP2200	Silicon Labs	10/100/1000 Base-T	TQFP-48		SPI

Fuente de alimentación principal
Regulador conmutado AC/UCCx813-xDC serie / Low-Power Economy BiCMOS Current-Mode PWM
UCC38C45 / UCCx8C4x BiCMOS Low-Power Current-Mode PWM Controller

Drivers para bus GPIB
GPIB bus transceivers
SN75ALS162, SN75160B	Octal General-Purpose Interface Bus Transceiver (Texas Instruments)
SN74LVC245A	Octal Bus Transceiver With 3-State Outputs
SN74ALS641A, SN74ALS642A, SN74AS641	Octal bus transceiver with open collector

Piezas mecánicas
Conector y receptáculo bus GPIB
SN	Descripción	Cant
553598-1	24 PIN CHAMP LATCH PLUG-SCREW / TE Connectivity	4
5554349-1	CONN CHAMP 24 POS RECEPTACLE / TE Connectivity	4
2-552076-1	KIT, COVER, 180 DEG, 24 POS / TE Connectivity	4
5553811-2	CONN RCPT 24POS R/A REV PCB / TE Connectivity	4
552283-1	ASSY, PLUG, 24 POS, B SLOT / TE Connectivity	4

Jack RJ45 con elementos magnéticos (Ethernet + transformador)

SN	Descripción	Cant
1-2301994-1	RJ45 JACK INT.MAG. 1GB LED 1X1 / TE Connectivity (llega en mayo)	4
2301994-3	RJ45 JACK INT.MAG. 10/100 1X1 IN / TE Connectivity (llega en mayo)	4

Otros reguladores conmutados
- UCC35705 High Speed Voltage Mode Pulse Width Modulator
- UC3844 Current-Mode PWM Controller
- UCC35706 High Speed Voltage Mode Pulse Width Modulator
- UCC28911 700V Flyback Switcher with Constant-Voltage Constant-Current and Primary-side Regulation
- UCC3813-3 Low Power Economy BiCMOS Current Mode PWM
- UCC25702 Advanced Voltage Mode Pulse Width Modulator
- UCC3813-4 Low Power Economy BiCMOS Current Mode PWM
- UCC35706 High Speed Voltage Mode Pulse Width Modulator

Componentes pasivos
Resistores
33	49,9	100	220	1k	1.5k	2.2k	4,7k	10k	100k	1Meg
2				2				4
USB	Eth		LEDs				I2C			XTAL

Capacitores
18p	22p	100p	100n	1u	2,2u	10u
			12			3
XTAL/USB	XTAL	XTAL	Des

Cristales
32.768 kHZ
RTC

Protección ESD
(Puerto USB)

Numero de parte	Fabricante
SP0503BAHT	Littelfuse

Pantallas LCD

Modelo	H020LB01	FRD280A3707E
Fabricante	Shenzhen Walin Technology Co., Ltd	Shenzhen Frida LCD
Dimension	2”	2.8”
Resolucion	320 x 240	240 x 320
Interfaz	MCU	MCU 16 bit
Pines	40	37
Depth color	262K	262k
Controlador	ILI9342C	ILI9341