Sockets depuración
Item	PN
1	6-102618-8	2 filas de 12P – 0.25mm
2	5-102699-7	2 filas 8P – 0,25 mm
3	535542-8	Receptáculo 2 filas 16P – 0,25 mm
4	535541-6	Receptáculo 1 filas 8P – 0,25 mm

2: Item 1

1: Item 2

3: Item 3

4: Item 4

Definición de buses

GPIB Port Expander [I2C] [PCA6408]
1	2	3	4	5	6	7
+5.0V	+3.3V	GND	SDA	SCL	/INT	/RESET

Viking Port Expander [SPI] [MC33996]
1	2	3	4	5	6	7	8	9
VPWR	VCC	GND_PWR	MOSI	MISO	SCLK	/CS	/RESET	PWM

Capacitive Keyboard [I2C] [PCF8885]
1	2	3	4	5	6	7	8
x	VCC	GND	SDA	SCL	A0	/INT	SLEEP

Lan Connection [SPI] [ENC28J60]
1	2	3	4	5	6	7	8
x	VCC (+3.3)	GND_PWR	MOSI	MISO	SCLK	/CS	/RESET

Port Expander 8 bit [I2C] [PCA6408A]
1	2	3	4	5	6	7	8
VDD(PORT)	VCC (I2C)	GND	SDA	SCL	ADDR	/INT	/RESET

Keyboard Port Expander 16 bit [I2C] [PCA6416A]
1	2	3	4	5	6	7	8
VDD(PORT)	VCC (I2C)	GND	SDA	SCL	ADDR	/INT	/RESET

LED Driver 15 bit [I2C] [PCA9952]
1	2	3	4	5	6	7	8
VCC(LED)	VDD(I2C)	GND	SDA	SCL	X	X	/RESET

Pic18 Pin Definitions

In Circuit Debbugger / In Circuit Serial Programming
Clock	Data	Reset
RB6	RB7	/MCLR / (pull up needed)
ICPGC	ICPGD	ICRST

Master Serial Synchronous Port
PIN	RB0	RB1	RB3	RC7
I2C	SDA	SCL
SPI	SDI	SCK	SDO	SDO / (conf alternativa)

Protección ESD + Transitorios
TVS

Part Number	Description	Quantity
SD05C-01FTG	TVS DIODE 5VWM 18VC SOD323	12
SD15C-01FTG	TVS DIODE 15VWM 31VC SOD323	12
SMAJ250CA	TVS DIODE 250VWM 405VC SMA	12
SP1003-01ETG	TVS DIODE 5VWM 12VC SOD882	12	30PF 30KV UNIDIRECTIONAL DISCRETE TVS-
SD24-01FTG	TVS DIODE 24VWM 42VC SOD323	6
SPHV24-01ETG	TVS DIODE 24VWM 50VC SOD882	24

Disposición espacial de tarjetas

Tarjeta madre

Tarjeta periferico

Conectores en angulo

Backplane

Tarjeta periferico

Tarjeta núcleo MCU