Sockets depuración
Item	PN
1	6-102618-8	2 filas de 12P – 0.25mm
2	5-102699-7	2 filas 8P – 0,25 mm
3	535542-8	Receptáculo 2 filas 16P – 0,25 mm
4	535541-6	Receptáculo 1 filas 8P – 0,25 mm

2: Item 1

1: Item 2

3: Item 3

4: Item 4

Definición de buses

GPIB Port Expander [I2C] [PCA6408]
1	2	3	4	5	6	7
+5.0V	+3.3V	GND	SDA	SCL	/INT	/RESET

Viking Port Expander [SPI] [MC33996]
1	2	3	4	5	6	7	8	9
VPWR	VCC	GND_PWR	MOSI	MISO	SCLK	/CS	/RESET	PWM

Capacitive Keyboard [I2C] [PCF8885]
1	2	3	4	5	6	7	8
x	VCC	GND	SDA	SCL	A0	/INT	SLEEP

Lan Connection [SPI] [ENC28J60]
1	2	3	4	5	6	7	8
x	VCC (+3.3)	GND_PWR	MOSI	MISO	SCLK	/CS	/RESET

Port Expander 8 bit [I2C] [PCA6408A]
1	2	3	4	5	6	7	8
VDD(PORT)	VCC (I2C)	GND	SDA	SCL	ADDR	/INT	/RESET

Keyboard Port Expander 16 bit [I2C] [PCA6416A]
1	2	3	4	5	6	7	8
VDD(PORT)	VCC (I2C)	GND	SDA	SCL	ADDR	/INT	/RESET

LED Driver 15 bit [I2C] [PCA9952]
1	2	3	4	5	6	7	8
VCC(LED)	VDD(I2C)	GND	SDA	SCL	X	X	/RESET

Pic18 Pin Definitions

In Circuit Debbugger / In Circuit Serial Programming
Clock	Data	Reset
RB6	RB7	/MCLR / (pull up needed)
ICPGC	ICPGD	ICRST

Master Serial Synchronous Port
PIN	RB0	RB1	RB3	RC7
I2C	SDA	SCL
SPI	SDI	SCK	SDO	SDO / (conf alternativa)

Protección ESD + Transitorios
TVS

Part Number	Description	Quantity
SD05C-01FTG	TVS DIODE 5VWM 18VC SOD323	12
SD15C-01FTG	TVS DIODE 15VWM 31VC SOD323	12
SMAJ250CA	TVS DIODE 250VWM 405VC SMA	12
SP1003-01ETG	TVS DIODE 5VWM 12VC SOD882	12	30PF 30KV UNIDIRECTIONAL DISCRETE TVS-
SD24-01FTG	TVS DIODE 24VWM 42VC SOD323	6
SPHV24-01ETG	TVS DIODE 24VWM 50VC SOD882	24

Estandares ESD
IEC 61000-4-2 ESD test voltage levels

Disposición espacial de tarjetas

Tarjeta madre

Tarjeta periferico

Conectores en angulo

Backplane

Tarjeta periferico

Tarjeta núcleo MCU

Diodos

Part Number	Description	Quantity Shipped
DST5100S	DIODE SCHOTTKY 100V 5A TO277B	10
DURB1640CT	DIODE RECTIFIER 8A 400V TO263	6
DURD560A	DIODE RECTIFIER 5A 600V TO252	10
MBRD10200CT	DIODE SCHOTTKY 200V 5A TO252	10
SD05C-01FTG	TVS DIODE 5VWM 18VC SOD323	12
SD15C-01FTG	TVS DIODE 15VWM 31VC SOD323	12
V230LA20AP	VARISTOR 360V 4.5KA DISC 14MM	12
V360CH8T	VARISTOR 360V 250A 2SMD	12